## Slide 1
MTS 6DOF Findings and Testing Summary (L231147 L5-S1)
Testing and Analysis Setup
  6 interventions x 3 motions (Flex/Ext, Lateral Bending, Axial Rotation)
  Third cycle extracted for each motion and intervention
  Linear stiffness from loading branch fit: M = k*theta + b
  Fit windows: FE 0.5-2.0 deg, LB 0.5-2.0 deg, AR 0.5-1.0 deg
  Additional metric: theta at 7.5 Nm on positive loading branch
Findings: Linear Stiffness Ranking (higher |k| = stiffer)
  Flexion/Extension: PUBF Left > Intact > FUF Left > FBF > Posterior Release > SPO
  Lateral Bending: PUBF Left > FUF Left > Intact > FBF > Posterior Release > SPO
  Axial Rotation: FUF Left > Intact > PUBF Left > FBF > Posterior Release > SPO
Findings: Theta at 7.5 Nm (lower theta = stiffer)
  Flexion/Extension: Intact > FUF Left > PUBF Left > Posterior Release > FBF > SPO
  Lateral Bending: PUBF Left > FUF Left > FBF > Posterior Release > Intact > SPO
  Axial Rotation: FUF Left > PUBF Left > Intact > FBF > Posterior Release > SPO